## Slide 1
CSE10/L • MODELING & SIMULATION
Flood Risk
Simulation System
Jade Valley Subdivision • Davao City, Philippines
D8 Flow Routing • HAND Model • PAGASA Storm Scenarios • Python-Based Simulation
3 Build Levels • 7 Storm Scenarios • 4 Prevention Measures • 5 Risk Zones
Jade Valley Flood Risk Project • 2026 • Davao City, Philippines

## Slide 2
01
Problem Definition & Objectives
Jade Valley Flood Risk Simulation • Problem Definition
PROBLEM STATEMENT
Jade Valley Subdivision in Davao City, Philippines, occupies 326.44 ha of predominantly flat terrain — 72.3% at slope below 5° — making it highly susceptible to both pluvial and fluvial flooding during heavy rainfall and typhoon events. Elevation ranges from 2.00 m to 71.75 m (mean 20.74 m). The combination of low mean elevation, flat relief, and proximity to river channels creates conditions where floodwater accumulates rapidly and drains slowly. Despite this risk, flood planning has lacked site-specific, terrain-accurate quantitative modeling. Critical questions remain unanswered: which zones flood first, at what rainfall threshold does inundation become critical, and how much protection can physical infrastructure provide? This simulation system directly addresses that gap through a Python-based, terrain-aware, scenario-driven flood model grounded in standard hydrological methods.
SIMULATION OBJECTIVES
1
Terrain-Accurate Flood Modeling
Model flood inundation over Jade Valley using D8 flow routing, Green-Ampt infiltration, and BFS river overflow dilation on a 57×61 DEM grid.
2
Multi-Scenario Storm Coverage
Simulate 6 PAGASA-calibrated storm scenarios from Light Rain (15 mm / 2 h) to Typhoon Signal 3 (400 mm / 18 h) plus a Custom scenario.
3
Risk Quantification — HAND Model
Classify all land cells into 5 risk zones (Very High → Safe) using the Height Above Nearest Drainage model with return-period flood thresholds.
4
Prevention Measure Evaluation
Evaluate 4 flood prevention measures via parallel baseline simulation, computing frame-by-frame flood extent and depth improvement deltas.
5
Interactive Visualization & Export
Provide animated visualization with live statistics, playback controls, and GIF animation / CSV time-series export for planning and research.

## Slide 3
02
System Architecture & Build Levels
Jade Valley Flood Risk Simulation • System Architecture
THREE PROGRESSIVE BUILD LEVELS
Build Level | Script | Measures | Description
25% Baseline | flood_simulation_25%.py | None | Pure hydrological baseline — unmitigated flood behavior as reference
50% Build | flood_simulation_50%.py | 2 Measures | Adds Riverbank Floodwall + Drainage Canal Network
75% Build | flood_simulation_75%.py | 4 Measures | Adds Retention Basin + Elevated Emergency Road on top of 50%
5-LAYER PIPELINE ARCHITECTURE
Layer 1 — Data
GeoTIFF DEM (57×61, 30.64 m/cell) + JPEG satellite background loaded from disk
Layer 2 — Input
Tkinter 2-tab GUI: storm scenario selection, prevention measure toggles & sliders
Layer 3 — Preprocessing
DEM modification → depression fill → D8 flow direction → flow accumulation → bank elevation
Layer 4 — Simulation
Frame-by-frame physics: rainfall → D8 routing (12 sub-iters) → BFS overflow → infiltration → drainage
Layer 5 — Output
Matplotlib 5-layer animation + live stats panel + GIF / CSV / .npy / risk map export
CORE FUNCTIONS & COMPONENTS
Function / Class | Role
load_dem() | Reads GeoTIFF, fills NoData, returns (dem, cellsize)
_fill_depressions() | Priority-Flood sink removal (Barnes et al. 2014)
_d8_flow_direction() | Steepest-descent D8 routing to 8 neighbours
_flow_accumulation() | Topological-sort upstream cell count
apply_floodwall() | Raises western bank cells by wall_height_m
apply_drainage_canal() | Lowers east/south corridor cells by canal_depth_m
apply_retention_basin() | Excavates basin in open land perimeter [75%]
apply_elevated_road() | Raises E-W emergency corridor [75%]
FloodSimulation | Class: holds state, runs all 5 physics ops per step
run_simulation() | Orchestrates preprocessing, loop, rendering, export

## Slide 4
03
Simulation Process Flow — 8 Stages
Jade Valley Flood Risk Simulation • Process Flow
1
Data Loading
GeoTIFF DEM loaded via rasterio. NoData cells filled. JPEG satellite background loaded. Cell size derived (~30.64 m). Elevation range: 2.00–71.75 m.
2
User Input GUI
2-tab Tkinter GUI: Tab 1 sets storm scenario, rainfall, duration, wind, soil saturation, drainage. Tab 2 toggles prevention measures with parameter sliders.
3
DEM Modification
Active prevention measures physically modify DEM before simulation starts: raises floodwall cells, lowers canal cells, excavates basin, raises road cells.
4
Hydrological Preprocessing
On modified DEM: depression fill → D8 flow direction → flow accumulation → stream mask → slope → runoff coefficient → infiltration → bank elevation.
5
Simulation Loop
Per timestep: rainfall intensity factor → add_rainfall() → route_water() (12 sub-iters) → apply_river_overflow() BFS → apply_infiltration() → apply_drainage().
6
Parallel Baseline
When prevention is active: identical simulation on the original unmodified DEM runs in parallel to compute flood reduction deltas for the stats panel.
7
Animation Rendering
5-layer Matplotlib composite: satellite BG + river band + rain depth (cyan→red) + river overflow (blue) + infrastructure overlays at zorder 6.
8
Output Export
GIF → Results/animations/ | CSV time-series → Results/data/ | Risk maps → Results/maps/ | .npy terrain arrays + flood_risk_report.txt.

## Slide 5
04
Simulation Setup & Terrain Analysis
Jade Valley Flood Risk Simulation • Terrain Analysis
STUDY AREA PARAMETERS
Parameter | Value
Location | Jade Valley, Davao City, Philippines
Grid | 57 rows × 61 columns
Cell Size | 30.64 m per cell
Total Area | 326.44 hectares
Elevation Range | 2.00 m – 71.75 m
Mean Elevation | 20.74 m
Mean Slope | 4.3°
Max Slope | 37.9°
TERRAIN SLOPE CLASSES
Slope Class | % Area | Behavior
Flat (<5°) | 72.3% | Primary runoff accumulation zone
Gentle (5–15°) | 21.9% | Moderate natural drainage
Steep (>15°) | 5.8% | Rapid drainage to channels
HYDROLOGICAL PREPROCESSING PIPELINE
Step | Operation | Description
a | NoData Filling | Nearest-neighbour interpolation replaces missing DEM pixels
b | DEM Smoothing | Gaussian filter (σ=0.5) reduces artificial roughness
c | Depression Filling | Priority-Flood algorithm (Barnes et al. 2014) removes sinks
d | D8 Flow Direction | Each cell assigned to steepest of 8 neighbours; diagonals use Euclidean distance
e | Flow Accumulation | Topological sort counts total upstream cells draining into each grid cell
f | Stream Delineation | Top 8% of flow accumulation (≥92nd percentile) → active river channel cells
g | Slope Computation | Gradient magnitude via numpy.gradient
h | Runoff Coefficient | Per-cell: clip(0.12 + 0.18×slope_norm + 0.12×scenario_factor, 0.12, 0.85)
i | Infiltration Capacity | Green-Ampt inspired: 1.2 + 1.2×elev_norm×(1−sat) − 0.7×scenario_factor
j | Bank Elevation Map | Min non-river neighbour elevation per river cell → flood_base_wse (median)

## Slide 6
05
Storm Scenarios — PAGASA Calibrated
Jade Valley Flood Risk Simulation • Storm Scenarios
7 STORM SCENARIO PRESETS
ID | Scenario Name | Rainfall | Duration | Pattern | Risk Context
1 | Light Rain | 15 mm | 2.0 h | Uniform | Annual minor event
2 | Moderate Rain | 36 mm | 3.0 h | Progressive | Frequent urban flooding
3 | Heavy Rain | 90 mm | 4.0 h | Progressive | Very High Risk threshold
4 | Typhoon Signal 1 | 150 mm | 8.0 h | Progressive | High Risk threshold
5 | Typhoon Signal 2 | 250 mm | 12.0 h | Burst | Medium Risk threshold
6 | Typhoon Signal 3 | 400 mm | 18.0 h | Burst | Low Risk threshold
7 | Custom | User def. | User def. | User def. | Research / planning
RAINFALL INTENSITY PATTERNS
Uniform
Constant 1.0× throughout storm duration
Progressive
Ramps from 0.40× to 1.40× (storm development)
Burst
Gaussian peak at 45% of duration, 0.30× to 1.80×
Decreasing
Heavy start tapering to 0.20× (convective event)
GUI SLIDER PARAMETERS
Parameter | Range | Default | Effect
Rainfall (mm) | 0 – 600 | 90 mm | Total storm precipitation
Duration (h) | 0.5 – 24.0 | 4.0 h | Storm event duration
Timestep (min) | 1 – 60 | 10 min | Simulation time increment
Wind Speed (km/h) | 0 – 200 | 0 | Modifies spatial rainfall distribution
Soil Saturation (%) | 0 – 100 | 30% | Initial soil moisture condition
Drainage Capacity (mm/hr) | 0 – 30 | 5.0 | Baseline grid drainage rate

## Slide 7
06
Risk Zone Classification — HAND Model Results
Jade Valley Flood Risk Simulation • Risk Zone Analysis
HAND MODEL METHODOLOGY
The Height Above Nearest Drainage (HAND) model computes the vertical distance from each terrain cell to the nearest drainage channel along the D8 flow path. Lower HAND values indicate higher flood susceptibility. Steps: NoData fill → Gaussian smoothing (σ=0.5) → Priority-Flood sink fill → D8 flow direction → flow accumulation → stream delineation (top 5%) → HAND computation → flood scenario mapping → 5-class risk zonation. Reference: Nobre et al. (2011) — Journal of Hydrology 404:13–29
RETURN PERIOD FLOOD SCENARIOS
Return Period | HAND Threshold | Flooded Area | % of Study | Mean Depth | Max Depth
5-Year | 1.0 m HAND | 51.64 ha | 15.8% | 0.73 m | 1.00 m
10-Year | 2.0 m HAND | 70.04 ha | 21.5% | 1.41 m | 2.00 m
25-Year | 3.5 m HAND | 90.03 ha | 27.6% | 2.43 m | 3.50 m
100-Year | 6.0 m HAND | 115.76 ha | 35.5% | 4.12 m | 6.00 m
5-CLASS RISK ZONE BREAKDOWN
Very High Risk
26.66 ha (8.2%)
Floods at Heavy Rain (≥90 mm). Mandatory evacuation during typhoons.
High Risk
31.83 ha (9.7%)
Floods at Typhoon Signal 1 (≥150 mm). Pre-evacuation alert.
Medium Risk
32.30 ha (9.9%)
Floods at Typhoon Signal 2 (≥250 mm). Monitor PAGASA advisories closely.
Low Risk
35.86 ha (11.0%)
Floods only at Typhoon Signal 3 (≥400 mm). Maintain standby status.
Safe Zone
174.81 ha (53.6%)
Above 100-year flood level. Suitable as official evacuation destination.
✔ 53.6% classified Safe Zone | Combined at-risk area = 38.9% (126.65 ha)

## Slide 8
07
Flood Prevention Measures
Jade Valley Flood Risk Simulation • Prevention Measures
Riverbank Floodwall
50% + 75% Builds
Red overlay on map
• Target: river bank cells at elevation ≤6 m within 3-cell dilation of river
• Action: raises those cells by wall_height_m (default 1.5 m, range 0.5–5.0 m)
• Effect: blocks river overflow until water surface exceeds wall crest by 2 cm
• Physics: floodwall cells block cross-wall transfers in route_water()
Drainage Canal Network
50% + 75% Builds
Cyan overlay on map
• Canal A: east-running corridor from lowest-elevation row to east boundary
• Canal B: south-running corridor from peak flow accumulation column to south
• Action: lowers corridor cells by canal_depth_m (default 2.0 m, range 0.5–5.0 m)
• Effect: fast drainage paths; canal cells drain 30× faster than base rate
Retention Basin
75% Build Only
Green overlay on map
• Target: highest flow accumulation zone in open land (outer perimeter only)
• Action: excavates circular depression (~6% of grid) by basin_depth_m (default 6 m)
• Constraint: residential core (inner 60% of grid) is excluded — no homes excavated
• Effect: stores peak runoff at topographic sink; reduces downstream inundation depth
Elevated Emergency Road
75% Build Only
Orange overlay on map
• Target: east-west corridor at ~45% grid height, skipping active river cells
• Action: raises corridor cells by road_height_m (default 1.5 m, range 0.5–3.0 m)
• Effect: maintains emergency vehicle access at design flood level
• Secondary: berm deflects surface flow laterally away from the central flood zone

## Slide 9
08
Key Findings & Simulation Outputs
Jade Valley Flood Risk Simulation • Key Findings
FLOOD RISK FINDINGS
72.3%
of the study area is flat terrain (slope <5°) — primary driver of runoff accumulation
8.2%
(26.66 ha) is Very High Risk — floods under Heavy Rain (≥90 mm)
17.9%
combined Very High + High Risk — 58.49 ha requiring priority infrastructure
35.5%
(115.76 ha) floods in 100-year event to a mean depth of 4.12 m
53.6%
(174.81 ha) is Safe Zone — suitable official evacuation destination
2.2×
flooded area growth from 5-year (51.64 ha) to 100-year (115.76 ha) events
SIMULATION SYSTEM OUTPUTS
Animated Visualization
5-layer Matplotlib: satellite BG + rain depth (cyan→red) + river overflow (blue) + infrastructure overlays
Live Statistics Panel
Per-frame: accumulated rainfall (mm), flooded area %, river overflow %, max depth (mm), vs-baseline delta
GIF Animation Export
Full animation exported to Results/animations/ — one GIF per simulation run
CSV Time-Series Export
Per-frame: time (min), rain_mm, flooded_pct, river_pct, max_depth_mm — baseline and prevention runs
Risk Map Files
HAND outputs: risk_map.npy, flood_risk_report.txt, flood_statistics.json, terrain .npy arrays
Playback Controls
Play/Pause, frame scrubber slider, speed control, step forward/backward buttons

## Slide 10
09
Conclusions & Recommendations
Jade Valley Flood Risk Simulation • Conclusions
CONCLUSIONS
• The system successfully models flood inundation using D8 flow routing, BFS river overflow, and Green-Ampt infiltration — providing terrain-accurate, scenario-driven results on real DEM data.
• HAND model confirms 8.2% Very High Risk (26.66 ha) flooding at Heavy Rain and 35.5% (115.76 ha) inundated in 100-year events — quantifying genuine flood risk for emergency planning.
• The Riverbank Floodwall effectively delays river overflow into the residential core by requiring water to overtop the raised crest before spreading onto adjacent land.
• The Drainage Canal Network accelerates runoff evacuation from the flood-prone central zone, reducing peak surface accumulation in slow-draining flat areas.
• The Retention Basin (75% build) provides the most significant peak inundation reduction by storing excess floodwater at the primary topographic sink before it spreads.
• The Elevated Emergency Road maintains critical cross-subdivision access for emergency vehicles at design flood level while deflecting surface flow laterally away from the central zone.
• The layered 4-measure strategy in the 75% build represents a comprehensive flood risk reduction approach aligned with the terrain and hydrology of Jade Valley Subdivision.
RECOMMENDATIONS
1
Prioritize drainage infrastructure upgrades in the Very High + High Risk zones (58.49 ha combined).
2
Implement early warning systems calibrated to HAND thresholds: 1.0 m (5-yr) and 2.0 m (10-yr).
3
Restrict high-density development in areas with HAND values below 1.0 m (Very High Risk zone).
4
Construct retention basins in designated open land at the outer perimeter to buffer storm runoff.
5
Install a riverbank floodwall along the western bank to delay typhoon-event inundation onset.
6
Designate the 53.6% Safe Zone (174.81 ha) as official evacuation areas with pre-positioned resources.
7
Conduct community flood drills aligned to PAGASA 5-year return period advisories.

## Slide 11
Thank You!
Questions & Discussion
326 ha
Total Study Area
Jade Valley Subdivision
7
Storm Scenarios
Light Rain → Typhoon Signal 3
4
Prevention Measures
Floodwall, Canal, Basin, Road
5
Risk Zones
Very High Risk → Safe Zone
Key Findings Summary
• 8.2% Very High Risk (26.66 ha) — floods at Heavy Rain ≥90 mm
• 17.9% combined High + Very High Risk — 58.49 ha requiring priority mitigation
• 35.5% of subdivision inundated in 100-year event (mean depth 4.12 m, max 6.00 m)
• 53.6% designated Safe Zone (174.81 ha) — suitable official evacuation destination
• 2.2× flooded area growth from 5-year (51.64 ha) to 100-year (115.76 ha) return period events
Jade Valley Flood Risk Simulation • CSE10/L • 2026 • Davao City, Philippines