## Slide 1
CSE10/L • Modeling & Simulation
Jade Valley Subdivision
Flood Risk Simulation System
Jade Valley Flood Risk Project • 2026 • Davao City, Philippines

## Slide 2
01
Introduction
Jade Valley Flood Risk Simulation • Introduction
Background
Jade Valley Subdivision is a residential community in Davao City, Philippines, situated on predominantly flat, low-lying terrain that is highly susceptible to flooding during heavy rainfall and tropical cyclone events. The area covers approximately 326.44 hectares with elevations ranging from 2.00 m to 71.75 m above mean sea level and a mean terrain elevation of 20.74 m. With 72.3 % of the land classified as flat (slope < 5°), surface runoff accumulates rapidly during storm events, exposing residents to both pluvial flooding from direct rainfall and fluvial flooding from nearby river overflow.
About This System
This system is an interactive, terrain-aware flood simulation built entirely in Python (NumPy, SciPy, rasterio, Matplotlib) and operates on a GeoTIFF Digital Elevation Model derived from topographic survey data of the subdivision. It models flood behavior under multiple storm scenarios and evaluates the effectiveness of flood prevention infrastructure.
Three Progressive Build Levels
— 25% Baseline — pure hydrological simulation with no mitigation; establishes the unmitigated flood baseline as a reference
— 50% Build — adds Riverbank Floodwall and Drainage Canal Network on top of the baseline
— 75% Build — adds Retention Basin and Elevated Emergency Road on top of the 50% build

## Slide 3
02
Problem Description
Jade Valley Flood Risk Simulation • Problem Description
The Flood Problem
Davao City is among the most flood-prone urban centers in Mindanao, Philippines, due to its proximity to river systems, high annual rainfall, and rapid urbanization of low-lying areas. Jade Valley Subdivision exemplifies the compounding flood risk faced by such communities. Its flat terrain limits natural drainage while proximity to river channels exposes residents to surface runoff accumulation and fluvial overflow during storm events. Despite this risk, flood planning for the subdivision has lacked a site-specific, terrain-accurate quantitative model — meaning emergency preparedness decisions and infrastructure investments have been made without direct evidence of how water moves across the terrain during actual storm conditions.
Critical Questions This Study Addresses
— Which specific zones within the subdivision flood first, and at what rainfall threshold does inundation become critical?
— How far does river overflow spread during storm events of varying intensities, and what water depth should residents expect?
— How much flood extent and peak depth reduction can physical prevention infrastructure achieve — and which combination of measures provides the best protection?
— Which areas can safely serve as evacuation zones during extreme flood events?
Scope and Significance
This simulation provides a terrain-aware, scenario-driven flood model grounded in standard hydrological methods, enabling planners and researchers to visualize flood progression, evaluate prevention measures, and identify risk zones with spatial precision — all derived from actual topographic survey data of Jade Valley Subdivision.

## Slide 4
03
Objectives
Jade Valley Flood Risk Simulation • Objectives
The simulation system is designed to meet the following objectives:
Obj 1 — Terrain-Accurate Flood Inundation Modeling
Model realistic flood inundation behavior over the Jade Valley terrain using physically-grounded hydrological methods — D8 flow routing, Green-Ampt-inspired infiltration, and BFS overflow dilation — applied directly to the GeoTIFF DEM.
Obj 2 — Multi-Scenario Storm Coverage
Simulate a range of storm scenarios from Light Rain (15 mm / 2 h) to Typhoon Signal 3 (400 mm / 18 h) so that flood risk can be assessed across multiple rainfall magnitudes and durations relevant to the Davao City context.
Obj 3 — Flood Risk Quantification and Zone Classification
Quantify flood risk across the subdivision using the HAND (Height Above Nearest Drainage) model and classify land into five risk zones — Very High, High, Medium, Low, and Safe — mapped against return-period flood thresholds.
Obj 4 — Prevention Measure Effectiveness Evaluation
Evaluate the effectiveness of four flood prevention measures — Riverbank Floodwall, Drainage Canal Network, Retention Basin, and Elevated Emergency Road — by running a parallel baseline simulation and computing frame-by-frame flood reduction deltas.
Obj 5 — Interactive Visualization and Data Export
Provide an interactive animated interface for visual observation of flood progression and prevention measure impact; export results as GIF animations and time-series CSV files to support planning and disaster preparedness decision-making.

## Slide 5
04
System Description
Jade Valley Flood Risk Simulation • System Description
Overview
The Jade Valley Flood Simulation is a Python-based desktop application that combines terrain analysis, hydrological modeling, and interactive visualization in a single self-contained system. It follows a five-layer pipeline architecture executed in sequence from raw DEM input through to animated output and data export.
Pipeline Layers
Data Layer
Reads the GeoTIFF DEM (57×61 cells, ~30.64 m/cell) and JPEG satellite background image from disk.
Input Layer
A two-tab Tkinter GUI collects storm scenario parameters and prevention measure settings before the simulation runs.
Preprocessing Layer
Applies any active prevention DEM modifications, then runs the full hydrological preprocessing pipeline (depression fill, D8 flow direction, flow accumulation, slope, runoff coefficient, infiltration capacity, bank elevation).
Simulation Engine
A frame-by-frame physics loop advances the flood state over time: rainfall addition → D8 water routing (12 sub-iterations) → BFS river overflow dilation → Green-Ampt infiltration → channel drainage.
Output Layer
Matplotlib renders a multi-layer animated visualization with a live statistics panel. Results are exportable as GIF animations, CSV time-series files, and static risk maps.

## Slide 6
05
Model Design
Jade Valley Flood Risk Simulation • Model Design
Per-Timestep Physics (5 Operations)
1. Rainfall Addition
Applies a rainfall intensity factor scaled by the storm pattern (uniform, progressive, burst, or decreasing), then adds rainfall to each cell weighted by its runoff coefficient and a wind-direction spatial map.
2. Water Routing
D8 diffusion distributes surface water across 8 neighbours in 12 sub-iterations per timestep. Transfer fraction is clipped between 0.03 and 0.35 based on local slope, capped at 20 % of the source cell’s water per sub-iteration.
3. River Overflow (BFS)
River water level rises each step proportionally to accumulated rainfall. A Breadth-First Search dilation then expands the flood front into adjacent cells whose terrain elevation falls below the current water surface elevation.
4. Infiltration
Soil saturation increases each step. A Green-Ampt-inspired formula removes water from rain_water and river_water at a rate proportional to remaining soil capacity.
5. Drainage
Channel cells drain at an elevated rate (base + 80×flow_weight² mm/hr). Canal cells drain 30× faster than the baseline rate. Very shallow residual water (< 4 mm) decays at 60–65 % per step.
Storm Scenarios
Scenario | Rainfall | Duration | Pattern
Light Rain | 15 mm | 2.0 h | Uniform
Moderate Rain | 36 mm | 3.0 h | Progressive
Heavy Rain | 90 mm | 4.0 h | Progressive
Typhoon Signal 1 | 150 mm | 8.0 h | Progressive
Typhoon Signal 2 | 250 mm | 12.0 h | Burst
Typhoon Signal 3 | 400 mm | 18.0 h | Burst
Custom | User | User | User
Prevention Measures
Measure | Build | Mechanism
Riverbank Floodwall | 50% + 75% | Raises river bank cells; blocks overflow until overtopped
Drainage Canal Network | 50% + 75% | Lowers E/S corridor; 30× faster drainage
Retention Basin | 75% only | Excavates depression in open outer-perimeter land
Elevated Emergency Road | 75% only | Raises E-W corridor; deflects surface flow laterally

## Slide 7
06
Assumptions
Jade Valley Flood Risk Simulation • Assumptions
The following assumptions and simplifications govern the simulation model. They are standard practice in raster-based hydrological simulation at this scale.
Single-Direction Flow (D8)
Each terrain cell routes water to exactly one of its eight neighbours — the steepest descent direction. Real flow may split across multiple paths; D8 is an accepted simplification in raster hydrology.
Static DEM
The DEM does not change during simulation. Erosion, sedimentation, and structural collapse are not modeled. Prevention measure modifications are applied once at the start and remain fixed throughout.
Uniform Soil Properties
Initial soil saturation is spatially uniform (user-specified). Elevation is used as a proxy for soil drainage class. Real soils vary in texture, porosity, and hydraulic conductivity across the site.
Simplified Infiltration
The infiltration model is inspired by Green-Ampt but is a scalar approximation. Capillary suction head, wetting front depth, and detailed soil hydraulics are not explicitly computed.
BFS Overflow Approximation
River overflow spreading uses Breadth-First Search dilation rather than a full shallow-water equation solver. This is computationally efficient and visually representative but does not model wave celerity or backwater effects.
Instantaneous Prevention Deployment
All prevention measures are fully effective from timestep 0. Construction time, soil settlement, and partial effectiveness during construction are not modeled.
No Groundwater Interaction
Subsurface flow, groundwater table rise, and sewer system interactions are excluded. This is a surface hydrology simulation only.
Constant Wind Field
Wind speed and direction are assumed constant throughout the storm duration. Spatial variation within the study area is not modeled.
Grid Resolution Limitation
The 57×61 grid at ~30.64 m/cell cannot resolve sub-cell features such as individual buildings, drainage pipes, or roads. Their effects are approximated through the runoff coefficient and drainage capacity parameters.
Retention Basin Instantaneous Fill
The retention basin stores water immediately once excavated in the DEM. Real effectiveness depends on inlet design, spillways, and outlet control structures not modeled here.

## Slide 8
07
Simulation Setup
Jade Valley Flood Risk Simulation • Simulation Setup
Software & Input Files
The simulation runs on Python 3.10 or higher inside a virtual environment. Required libraries: NumPy, SciPy, Matplotlib, rasterio, Pillow, and pandas. The mandatory input files are the GeoTIFF DEM (JVS_Simulation.tif) and the JPEG satellite background (JVS_2D.jpg), both located in the Map Topography folder.
How to Run
— Baseline only: python "Main/flood_simulation_25%.py"
— With 2 measures: python "Main/flood_simulation_50%.py"
— With 4 measures: python "Main/flood_simulation_75%.py"
Output Files
— Results/animations/ — GIF animation for each run
— Results/data/ — CSV time-series, .npy terrain arrays, risk report
— Results/maps/ — static risk zone and HAND model map images
Key Numerical Configuration
Parameter | Value
DEM Grid | 57 rows × 61 columns
Cell Size | 30.64 m
Total Area | 326.44 ha
Elevation Range | 2.00 – 71.75 m (mean 20.74 m)
Stream Threshold | Top 8% of flow accumulation (92nd percentile)
Routing Sub-iters | 12 per timestep
BFS Hops | 1 (light) → 2 (moderate) → 4–6 (typhoon)
GUI Operation Sequence
Step 1 — Select Scenario
Choose a storm preset from the dropdown (Scenarios 1–6) or select Custom (Scenario 7) and manually enter rainfall and duration.
Step 2 — Adjust Parameters
Set Timestep, Wind Speed/Direction, Soil Saturation, Drainage Capacity, and Rainfall Pattern using the sliders provided.
Step 3 — Configure Prevention Measures
(50 % / 75 % builds only) Switch to the Prevention Measures tab, toggle desired measures ON, and adjust their depth or height parameters.
Step 4 — Run
Click RUN. The GUI closes, preprocessing runs in the console, and the animated figure window opens automatically when ready.
Step 5 — Interact with Playback
Use Play/Pause, the frame scrubber, speed slider, and step buttons to explore any point in the simulation timeline.
Step 6 — Export
Click SAVE GIF or SAVE CSV to export the animation or time-series data to the Results folder.

## Slide 9
08
Results and Analysis
Jade Valley Flood Risk Simulation • Results and Analysis
HAND Model Risk Zone Classification
The Height Above Nearest Drainage (HAND) model was applied to classify every terrain cell by flood susceptibility. Five risk zones were identified based on HAND thresholds corresponding to storm return periods:
Risk Zone | Area | % of Total | Flood Threshold
Very High | 26.66 ha | 8.2% | Floods at Heavy Rain (≥90 mm)
High | 31.83 ha | 9.7% | Floods at Typhoon Signal 1 (≥150 mm)
Medium | 32.30 ha | 9.9% | Floods at Typhoon Signal 2 (≥250 mm)
Low | 35.86 ha | 11.0% | Floods at Typhoon Signal 3 (≥400 mm)
Safe | 174.81 ha | 53.6% | Above 100-year flood level
Return Period Flood Extents
Scenario | Flooded Area | % Area | Mean Depth | Max Depth
5-Year (1.0 m HAND) | 51.64 ha | 15.8% | 0.73 m mean | 1.00 m max
10-Year (2.0 m HAND) | 70.04 ha | 21.5% | 1.41 m mean | 2.00 m max
25-Year (3.5 m HAND) | 90.03 ha | 27.6% | 2.43 m mean | 3.50 m max
100-Year (6.0 m HAND) | 115.76 ha | 35.5% | 4.12 m mean | 6.00 m max
Flooded area grows 2.2× from the 5-year to the 100-year event. Mean depth increases from 0.73 m to 4.12 m.
Prevention Measure Findings
Riverbank Floodwall
Effectively delays river overflow into the residential core. Water must overtop the raised crest before spreading onto adjacent land, buying critical time for evacuation during typhoon events.
Drainage Canal Network
Accelerates runoff evacuation from the flat central zone. Canal cells drain 30× faster than the base rate, significantly reducing peak rain_water accumulation in areas that would otherwise drain slowly.
Retention Basin (75% Build)
Provides the most significant reduction in peak inundation depth by capturing excess floodwater at the primary topographic sink before it spreads over residential land. Sited in open outer-perimeter land to avoid displacing any existing structures.
Elevated Emergency Road (75% Build)
Maintains critical cross-subdivision access for emergency vehicles at design flood level. The raised berm also deflects surface flow laterally, reducing water pooling in the central zone.

## Slide 10
09
Recommendations
Jade Valley Flood Risk Simulation • Recommendations
Based on the simulation results and HAND model risk zone classification, the following recommendations are proposed to reduce flood risk in Jade Valley Subdivision:
1. Priority Infrastructure Upgrades
Drainage infrastructure upgrades should be prioritized in the Very High and High Risk zones, which together cover 58.49 ha (17.9 %) of the subdivision. These areas experience flooding at rainfall thresholds as low as 90 mm and require immediate action.
2. Early Warning Systems
Flood early warning systems should be calibrated to HAND thresholds: issue an advisory when accumulation approaches the 1.0 m level (5-year scenario) and trigger evacuation orders at the 2.0 m level (10-year scenario).
3. Regulated Land Use
High-density residential development and critical infrastructure should be restricted in areas with HAND values below 1.0 m. These Very High Risk cells are the first to flood and sustain the deepest inundation during storm events.
4. Retention Basin Construction
Retention basins should be constructed in designated open land at the outer perimeter of the subdivision. Siting must avoid the residential core, as demonstrated in the 75 % build model, where the basin was placed in the outer 20 % of the grid.
5. Riverbank Floodwall Installation
A riverbank floodwall should be installed along the western bank channel. Minimum design height should correspond to the 10-year return period flood level (2.0 m HAND threshold) to provide meaningful protection against frequent events.
6. Evacuation Zone Designation
The 53.6 % Safe Zone (174.81 ha) above the 100-year flood level should be formally designated as official evacuation areas, with pre-positioned emergency supplies and clearly marked access routes connecting at-risk zones to safe elevated ground.
7. Community Flood Preparedness
Community flood drills and education programs should familiarize residents with risk zone classifications. Distributing risk zone maps showing Very High, High, Medium, and Low Risk areas relative to residents’ homes will improve preparedness.

## Slide 11
Thank You
Questions & Discussion
326 ha
Total Study Area
7
Storm Scenarios
4
Prevention Measures
5
Risk Zones
Key Findings
— 8.2 % Very High Risk (26.66 ha) — floods at Heavy Rain ≥90 mm
— 17.9 % combined High + Very High Risk — 58.49 ha requiring priority mitigation
— 35.5 % of subdivision inundated in the 100-year event (mean depth 4.12 m)
— 53.6 % designated Safe Zone (174.81 ha) — suitable official evacuation destination
— Flooded area grows 2.2× from the 5-year to the 100-year return period event
Jade Valley Flood Risk Simulation • CSE10/L • 2026 • Davao City, Philippines