## Slide 1
FINAL PROJECT | SIMULATION SYSTEM
FLOOD RISK SIMULATION
JADE VALLEY MODEL
A TERRAIN-AWARE HYDROLOGICAL SIMULATION SYSTEM
D8 FLOW ROUTING | GREEN-AMPT INFILTRATION | BFS RIVER OVERFLOW
DOCUMENTATION + RESULTS | COMPILED FROM SIMULATION SYSTEM OUTPUTS
01 / 39

## Slide 2
00 CONTENTS
2 / 39
TABLE OF CONTENTS
01
Introduction
02
Problem Definition
03
Objectives
04
System Description
05
System Flow
06
System Variables
07
Assumptions
08
Simulation Setup
09
Results
10
Conclusion

## Slide 3
01
INTRODUCTION
3 / 39

## Slide 4
01 INTRODUCTION
4 / 39
PROJECT CONTEXT
Jade Valley Subdivision is a residential community in Davao City, Philippines, situated on low-lying terrain that is highly susceptible to flooding during heavy rainfall events and tropical cyclones.
The study area covers approximately 326.44 hectares with elevations ranging from 2.00 m to 71.75 m above mean sea level, mean elevation of 20.74 m. With 72.3% of the land classified as flat (slope < 5°), surface runoff accumulates rapidly during storms, exposing the subdivision to both pluvial flooding from direct rainfall and fluvial flooding from nearby river overflow.
This system is an interactive, terrain-aware flood simulation built entirely in Python (rasterio, NumPy, SciPy, Matplotlib) operating on a GeoTIFF Digital Elevation Model (DEM) derived from 3D topographic survey data of the subdivision.

## Slide 5
01 INTRODUCTION
5 / 39
JADE VALLEY FLOOD SIMULATION | DAVAO CITY, PHILIPPINES
FINAL BUILD 100%
THREE PROGRESSIVE BUILDS + MASTER
25% Baseline simulation. No prevention measures. Establishes the unmitigated flood behaviour as the reference for comparison.
50% Adds two prevention measures: Riverbank Floodwall and Drainage Canal Network. Runs an improved and a baseline simulation in parallel and reports the delta.
75% Adds two further measures: Retention Basin and Elevated Emergency Road. Renders all four infrastructure overlays on the animated map.
100% Complete system. Same GUI as 75% (storm tab + four prevention measures) PLUS a COLLECT ALL DATA button that runs the full 6 × 4 = 24 scenario/config matrix and exports the master data tables that drive this presentation.

## Slide 6
02
PROBLEM DEFINITION
6 / 39

## Slide 7
02
PROBLEM DEFINITION
6 / 39
Why Jade Valley is flood-prone, the planning gap this system addresses, and the critical questions a terrain-aware model can answer.

## Slide 8
02 PROBLEM DEFINITION
7 / 39
WHY JADE VALLEY FLOODS
Davao City is among the most flood-prone urban centres in the Philippines: proximity to river systems, high annual rainfall, and rapid urbanisation of low-lying areas.
Jade Valley exemplifies the compounding flood risk in such communities: flat terrain limits natural drainage while proximity to river channels exposes residents to both surface runoff accumulation and fluvial overflow during storm events.
Despite these conditions, flood risk planning in residential subdivisions often lacks site-specific quantitative modeling — meaning emergency preparedness, infrastructure investments, and land use recommendations are made without direct evidence of how water actually moves across the terrain during real storms.

## Slide 9
02 PROBLEM DEFINITION
8 / 39
QUESTIONS THIS SYSTEM ANSWERS
Q1 Which specific zones flood first, and at what rainfall threshold does inundation become critical?
Q2 How far does river overflow spread across the subdivision during typhoons of varying intensities?
Q3 How much flood extent and peak depth reduction can be achieved by constructing prevention infrastructure — and which combination provides the best protection?
Q4 Which areas can safely serve as evacuation zones during a 100-year flood event?
This simulation system answers each of these questions with a terrain-aware, scenario-driven model grounded in standard hydrological methods.

## Slide 10
03
SECTON
OBJECTIVES
Six concrete objectives the simulation system is designed to meet.
JADE VALLEY FLOOD SIMULATION | DAVAO CITY
9 / 39

## Slide 11
03 OBJECTIVES
10 / 39
JADE VALLEY FLOOD SIMULATION | DAVAO CITY, PHILIPPINES
FINAL BUILD 100%
SIX OBJECTIVES
3.1 Terrain-Accurate Flood Inundation Modeling — D8 flow routing, Green-Ampt infiltration, BFS overflow dilation.
3.2 Multi-Scenario Storm Coverage — PAGASA-calibrated scenarios from Light Rain (15 mm / 2 h) to Typhoon Signal 3 (400 mm / 18 h).
3.3 Flood Risk Quantification — five-class HAND-based risk zonation (Very High / High / Medium / Low / Safe).
3.4 Prevention Measure Evaluation — frame-by-frame comparison of baseline vs. improved runs across four mitigation configurations.
3.5 Interactive Visualisation — animated multi-layer figure with playback controls.
3.6 Data Export — GIF animations, time-series CSV files, .npy terrain arrays, JSON statistics, and human-readable reports.

## Slide 12
04
SYSTEM DESCRIPTION
Architecture, build hierarchy, core components, and data flow.
JADE VALLEY FLOOD SIMULATION | DAVAO CITY
11 / 39

## Slide 13
04 SYSTEM DESCRIPTION
12 / 39
JADE VALLEY FLOOD SIMULATION | DAVAO CITY, PHILIPPINES
FINAL BUILD 100%
ARCHITECTURE: FIVE LOGICAL LAYERS
LAYER 1 Data Layer | Reads the GeoTIFF DEM and JPEG satellite background from disk. All terrain computations derive from the 57 × 61 elevation grid.
LAYER 2 Input Layer | A Tkinter GUI collects storm parameters and prevention settings (the 100% build skips this and runs the matrix headlessly).
LAYER 3 Preprocessing Layer | Applies prevention DEM modifications, then runs the hydrological pipeline: depression fill, D8 flow direction, flow accumulation, slope, runoff coefficient, infiltration capacity, bank elevation map.
LAYER 4 Simulation Engine | Frame-by-frame physics loop: rainfall addition, water routing, river overflow via BFS dilation, infiltration, drainage. Parallel baseline sim runs simultaneously when prevention is active.
LAYER 5 Output Layer | Matplotlib renders the animation; results export as GIF animations and CSV/JSON/.npy artefacts.

## Slide 14
04 SYSTEM DESCRIPTION
13 / 39
JADE VALLEY FLOOD SIMULATION | DAVAO CITY, PHILIPPINES
FINAL BUILD 100%
BUILD HIERARCHY
BUILD SCRIPT PREVENTION MEASURES
--------------------------------------------------------------------------------
25% Baseline flood_simulation_25%.py None
50% Two-meas. flood_simulation_50%.py Floodwall + Drainage Canal
75% Four-meas flood_simulation_75%.py Floodwall + Canal +
Retention Basin + Elevated Road
100% Master flood_simulation_100%.py Headless 6 × 4 matrix runner
+ HAND/risk-zone analysis

## Slide 15
04 SYSTEM DESCRIPTION
14 / 39
JADE VALLEY FLOOD SIMULATION | DAVAO CITY, PHILIPPINES
FINAL BUILD 100%
CORE COMPONENTS
load_dem() Reads GeoTIFF; fills NoData; returns (dem, cellsize)
_fill_depressions() Priority-Flood sink removal
_d8_flow_direction() Steepest-descent D8 routing
_flow_accumulation() Topological-sort upstream count
build_stream_mask() Top-8% accumulation = river channel
apply_floodwall() DEM modification: raises western bank cells
apply_drainage_canal() DEM modification: lowers east/south corridors
apply_retention_basin() DEM modification: excavates basin depression [75%]
apply_elevated_road() DEM modification: raises emergency road berm [75%]
apply_prevention_measures() Combines active measures into one modified DEM
FloodSimulation Class — holds state; runs physics per timestep
.add_rainfall() Runoff-weighted rainfall onto grid
.route_water() D8 surface-water diffusion (12 sub-iters)
.apply_river_overflow() BFS dilation of flood front from channel
.apply_infiltration() Green-Ampt inspired soil absorption
.apply_drainage() Channel + canal drainage removal
.step() Calls all five methods for one timestep
wind_rainfall_map() Wind-modified spatial rainfall weights
run_simulation() Orchestrates preprocessing, loop, rendering
SimulationGUI Tkinter two-tab GUI

## Slide 16
04 SYSTEM DESCRIPTION
15 / 39
JADE VALLEY FLOOD SIMULATION | DAVAO CITY, PHILIPPINES
FINAL BUILD 100%
DATA FLOW
GeoTIFF DEM
|
+-- Prevention DEM modifications (if enabled)
|
+-- Hydrological preprocessing --> fdir, accum, river_mask,
| slope, runoff_coeff,
| max_inf, bank_elev
|
+-- [Improved Sim] FloodSimulation(modified_dem) -+
| frame loop x num_frames +-- Animation
+-- [Baseline Sim] FloodSimulation(original_dem) -+ + CSV Export

## Slide 17
05
SYSTEM FLOW
The eight stages from terrain loading through to output export.
JADE VALLEY FLOOD SIMULATION | DAVAO CITY
16 / 39

## Slide 18
05 SYSTEM FLOW
17 / 39
JADE VALLEY FLOOD SIMULATION | DAVAO CITY, PHILIPPINES
FINAL BUILD 100%
STAGES 1–4: LOAD, INPUT, PREVENTION, PREPROCESS
STAGE 1 Data Loading | Read GeoTIFF DEM (rasterio) and JPEG background (Pillow). Resize JPEG to ≤ 2048 px on longest side. Cell size corrected via cosine-latitude scaling.
STAGE 2 User Input | Two-tab Tkinter GUI gathers storm parameters and prevention settings. 100% build skips this stage and uses CLI flags / defaults.
STAGE 3 DEM Modification | For each active measure, modify elevations on target cells: raise floodwall, lower canals, excavate retention basin, raise emergency road.
STAGE 4 Hydrological Preprocessing | Priority-Flood fill, D8 flow direction, flow accumulation, stream mask, slope, runoff coefficient, infiltration capacity, bank-elevation map.

## Slide 19
05 SYSTEM FLOW
18 / 39
JADE VALLEY FLOOD SIMULATION | DAVAO CITY, PHILIPPINES
FINAL BUILD 100%
STAGE 5: PER-TIMESTEP LOOP
The simulation loop runs num_frames = ceil(duration_h / timestep_h) iterations. At each timestep, six physics operations execute in order:
STEP 1 Rainfall intensity factor scales rate by storm pattern (uniform / progressive / burst / decreasing).
STEP 2 add_rainfall(): rain × intensity × dt × runoff_coeff × wind_map.
STEP 3 route_water(): D8 surface diffusion, 12 sub-iterations.
STEP 4 apply_river_overflow(): rises river level; BFS dilation expands flood front; floodwall blocks overflow until overtopped; canal cells receive 40% less river water.
STEP 5 apply_infiltration(): saturation grows; infiltration removes water (Green-Ampt inspired).
STEP 6 apply_drainage(): base + channel + canal drainage; shallow water decays.

## Slide 20
05 SYSTEM FLOW
19 / 39
JADE VALLEY FLOOD SIMULATION | DAVAO CITY, PHILIPPINES
FINAL BUILD 100%
STAGES 6–8: BASELINE, RENDER, EXPORT
STAGE 6 Parallel Baseline Run | When prevention is enabled, an identical sim runs on the unmodified DEM with no measures; deltas feed the live stats panel.
STAGE 7 Animation Rendering | Five composited Matplotlib layers: satellite background, river channel band, rain depth, river overflow, prevention overlays.
STAGE 8 Output Export | GIF animation, time-series CSVs, and (via the 100% build) master_results_table.csv/.json, master_results_summary.txt, master_reduction_table.txt, plus the HAND/risk-zone artefacts.

## Slide 21
06
SYSTEM VARIABLES
Inputs, prevention parameters, terrain arrays, and storm presets.
JADE VALLEY FLOOD SIMULATION | DAVAO CITY
20 / 39

## Slide 22
06 SYSTEM VARIABLES
21 / 39
JADE VALLEY FLOOD SIMULATION | DAVAO CITY, PHILIPPINES
FINAL BUILD 100%
USER INPUT VARIABLES
rainfall_mm 0–600 mm | Total storm rainfall.
duration_h 0.5–24.0 h | Storm duration.
timestep_min 1–60 min | Simulation timestep.
wind_speed 0–200 km/h | Wind speed.
wind_dir 0–360° | Wind direction.
soil_sat_pct 0–100 % | Initial soil saturation.
drain_cap 0–30 mm/hr | Baseline drainage capacity.
pattern uniform / progressive / burst / decreasing
start_time HH:MM | Clock time at frame 0.

## Slide 23
06 SYSTEM VARIABLES
22 / 39
JADE VALLEY FLOOD SIMULATION | DAVAO CITY, PHILIPPINES
FINAL BUILD 100%
PREVENTION MEASURE VARIABLES
use_floodwall / wall_height_m Riverbank Floodwall, crest 0.5–5.0 m (default 1.5 m).
use_canal / canal_depth_m Drainage Canal Network, depth 0.5–5.0 m (default 2.0 m).
use_basin / basin_depth_m [75% / 100%] Retention Basin, depth 2.0–10.0 m (default 6.0 m).
use_road / road_height_m [75% / 100%] Elevated Emergency Road, raise 0.5–3.0 m (default 1.5 m).

## Slide 24
06 SYSTEM VARIABLES
23 / 39
JADE VALLEY FLOOD SIMULATION | DAVAO CITY, PHILIPPINES
FINAL BUILD 100%
STORM SCENARIO PRESETS
ID NAME RAINFALL DURATION PATTERN
--------------------------------------------------------------------------------
1 Light Rain 15 mm 2.0 h uniform
2 Moderate Rain 36 mm 3.0 h progressive
3 Heavy Rain 90 mm 4.0 h progressive
4 Typhoon Signal 1 (Tropical Depression) 150 mm 8.0 h progressive
5 Typhoon Signal 2 (Tropical Storm) 250 mm 12.0 h burst
6 Typhoon Signal 3 (Severe Typhoon) 400 mm 18.0 h burst
7 Custom user def user def user def

## Slide 25
07
ASSUMPTIONS
Modeling simplifications, scope limitations, and what is not simulated.
JADE VALLEY FLOOD SIMULATION | DAVAO CITY
24 / 39

## Slide 26
07 ASSUMPTIONS
25 / 39
JADE VALLEY FLOOD SIMULATION | DAVAO CITY, PHILIPPINES
FINAL BUILD 100%
MODELING ASSUMPTIONS
5.1 Single-Direction Flow — D8: each cell routes to one of 8 neighbours (steepest descent).
5.2 Static DEM — no erosion/sedimentation; prevention measures are applied once before t=0.
5.3 Uniform Initial Soil Saturation — spatially uniform; infiltration capacity uses elevation as proxy.
5.4 Simplified Green-Ampt Infiltration — scalar approximation; no explicit wetting front.
5.5 BFS River Overflow — efficient dilation; not a full shallow-water equation solver.
5.6 Instantaneous Prevention Deployment — measures are fully effective from t=0.
5.7 No Groundwater Interaction — surface hydrology only.
5.8 Wind Uniformity — constant throughout the storm.
5.9 PAGASA-Calibrated Scenarios — Mindanao / Davao classification.
5.10 Retention Basin — instantaneous fill, no inlet/spillway model.
5.11 Grid Resolution — ~30.64 m / cell; sub-grid features approximated via runoff coefficient and drainage capacity.

## Slide 27
08
SIMULATION SETUP
Software requirements, inputs, run procedures, and numerical config.
JADE VALLEY FLOOD SIMULATION | DAVAO CITY
26 / 39

## Slide 28
08 SIMULATION SETUP
27 / 39
JADE VALLEY FLOOD SIMULATION | DAVAO CITY, PHILIPPINES
FINAL BUILD 100%
SOFTWARE + INPUTS
Python 3.10 or higher
Virtual env .venv (project root)
Required pkgs numpy scipy matplotlib rasterio Pillow ezdxf pysheds pandas python-pptx python-docx
Required Map Topography/3D/JVS_Simulation.tif (GeoTIFF DEM)
Required Map Topography/2D/JVS_2D.jpg (background)
Optional Map Topography/2D/...2D_vectorial.dxf (vector overlay)
Optional Map Topography/3D/...3D_modeling.dxf (3D reference)

## Slide 29
08 SIMULATION SETUP
28 / 39
JADE VALLEY FLOOD SIMULATION | DAVAO CITY, PHILIPPINES
FINAL BUILD 100%
RUNNING THE SYSTEM
25% (GUI) python "Main/flood_simulation_25%.py" # baseline only
50% (GUI) python "Main/flood_simulation_50%.py" # + Wall + Canal
75% (GUI) python "Main/flood_simulation_75%.py" # + Basin + Road
100% (GUI+matrix) python "Main/flood_simulation_100%.py" # full system
100% headless python "Main/flood_simulation_100%.py" --matrix-only
HAND analysis python "Main/hand_risk_analysis.py" # idempotent
Reality check python "Main/run_validation.py" # vs historical events

## Slide 30
08 SIMULATION SETUP
29 / 39
JADE VALLEY FLOOD SIMULATION | DAVAO CITY, PHILIPPINES
FINAL BUILD 100%
NUMERICAL CONFIGURATION
DEM Grid : 57 rows × 61 cols
Cell Size : 30.64 m
Total Study Area : 326.44 ha
Elevation Range : 2.00 m – 71.75 m
Mean Elevation : 20.74 m
Mean Slope : 4.3°
Stream Threshold : Top 8% of flow accumulation (92nd pctile)
HAND Smooth Sigma : 0.5
Curve Number : 85 (urban mix reference)
Routing Sub-steps : 12 D8 iterations per timestep
River Overflow BFS Hops : 1 (light) to 4-6 (typhoon)
Matrix Timestep : 20 min (100% build default)

## Slide 31
09
RESULTS
Risk zonation, return-period analysis, and the 24-cell master dataset.
JADE VALLEY FLOOD SIMULATION | DAVAO CITY
30 / 39

## Slide 32
09 RESULTS
31 / 39
JADE VALLEY FLOOD SIMULATION | DAVAO CITY, PHILIPPINES
FINAL BUILD 100%
HAND RISK ZONES
The HAND (Height Above Nearest Drainage) model classifies every terrain cell into one of five risk zones:
VERY HIGH 26.66 ha (8.2%) — Floods in Heavy Rain ≥ 90 mm. Mandatory evacuation during typhoons.
HIGH 31.83 ha (9.7%) — Floods in Typhoon Signal 1 ≥ 150 mm. Pre-evacuation alert.
MEDIUM 32.30 ha (9.9%) — Floods in Typhoon Signal 2 ≥ 250 mm. Monitor advisories.
LOW 35.86 ha (11.0%) — Floods only in extreme events (Sig 3 / ≥ 400 mm). Standby.
SAFE 174.81 ha (53.6%) — Above 100-yr flood level. Suitable as evacuation destination.

## Slide 33
09 RESULTS
32 / 39
JADE VALLEY FLOOD SIMULATION | DAVAO CITY, PHILIPPINES
FINAL BUILD 100%
RETURN PERIOD ANALYSIS
5-YEAR HAND threshold 1.0 m — 51.64 ha (15.8%) flooded — mean depth 0.73 m.
10-YEAR HAND threshold 2.0 m — 70.04 ha (21.5%) flooded — mean depth 1.41 m.
25-YEAR HAND threshold 3.5 m — 90.03 ha (27.6%) flooded — mean depth 2.43 m.
100-YEAR HAND threshold 6.0 m — 115.76 ha (35.5%) flooded — mean depth 4.12 m.
These results underline the severity of the 100-year design event (35.5% of the subdivision inundated) and the rationale for the layered prevention strategy evaluated by the simulation matrix.

## Slide 34
09 RESULTS
33 / 39
MASTER RESULTS: ALL 24 RUNS
Scenario | Config | Peak % | Peak ha | Max Depth mm | River % | Onset min
Light Rain | Baseline | 0.0 | 0.0 | 0 | 0.0 | —
Light Rain | Wall+Canal | 0.0 | 0.0 | 0 | 0.0 | —
Light Rain | Full Prevention | 0.0 | 0.0 | 0 | 0.0 | —
Light Rain | Large Prevention | 0.0 | 0.0 | 0 | 0.0 | —
Moderate Rain | Baseline | 21.43 | 69.94 | 214 | 21.17 | 160
Moderate Rain | Wall+Canal | 16.36 | 53.42 | 217 | 16.19 | 160
Moderate Rain | Full Prevention | 14.15 | 46.19 | 218 | 13.98 | 160
Moderate Rain | Large Prevention | 12.65 | 41.31 | 217 | 12.74 | 160
Heavy Rain | Baseline | 39.09 | 127.58 | 1344 | 34.83 | 120
Heavy Rain | Wall+Canal | 33.68 | 109.93 | 1431 | 28.65 | 120
Heavy Rain | Full Prevention | 30.89 | 100.83 | 1471 | 25.11 | 120
Heavy Rain | Large Prevention | 28.73 | 93.79 | 1438 | 23.76 | 120
Sig 1 (TD) | Baseline | 44.92 | 146.64 | 3001 | 39.83 | 160
Sig 1 (TD) | Wall+Canal | 42.45 | 138.57 | 3241 | 36.09 | 160
Sig 1 (TD) | Full Prevention | 39.98 | 130.49 | 3258 | 32.7 | 160
Sig 1 (TD) | Large Prevention | 37.91 | 123.74 | 3243 | 31.35 | 160
Sig 2 (TS) | Baseline | 49.7 | 162.23 | 3315 | 46.33 | 180
Sig 2 (TS) | Wall+Canal | 47.08 | 153.68 | 3666 | 42.62 | 180
Sig 2 (TS) | Full Prevention | 44.2 | 144.3 | 3738 | 38.22 | 180
Sig 2 (TS) | Large Prevention | 42.19 | 137.72 | 3680 | 36.99 | 180
Sig 3 (Severe) | Baseline | 56.46 | 184.29 | 3565 | 50.47 | 200
Sig 3 (Severe) | Wall+Canal | 53.98 | 176.21 | 3859 | 46.88 | 200
Sig 3 (Severe) | Full Prevention | 50.3 | 164.2 | 3953 | 42.34 | 200
Sig 3 (Severe) | Large Prevention | 49.12 | 160.35 | 3878 | 41.04 | 200

## Slide 35
09 RESULTS
35 / 39
REDUCTION VS BASELINE
Scenario | Config | Δ Flooded % | Δ Flooded ha | Δ Depth mm | Reduction %
Light Rain | Wall+Canal | +0.00 | +0.00 | +0 | +0.0%
Light Rain | Full Prevention | +0.00 | +0.00 | +0 | +0.0%
Light Rain | Large Prevention | +0.00 | +0.00 | +0 | +0.0%
Moderate Rain | Wall+Canal | -5.07 | -16.52 | +2 | -23.7%
Moderate Rain | Full Prevention | -7.28 | -23.75 | +3 | -34.0%
Moderate Rain | Large Prevention | -8.78 | -28.63 | +2 | -41.0%
Heavy Rain | Wall+Canal | -5.41 | -17.65 | +86 | -13.8%
Heavy Rain | Full Prevention | -8.20 | -26.75 | +127 | -21.0%
Heavy Rain | Large Prevention | -10.36 | -33.79 | +93 | -26.5%
Sig 1 (TD) | Wall+Canal | -2.47 | -8.07 | +239 | -5.5%
Sig 1 (TD) | Full Prevention | -4.94 | -16.15 | +257 | -11.0%
Sig 1 (TD) | Large Prevention | -7.01 | -22.90 | +242 | -15.6%
Sig 2 (TS) | Wall+Canal | -2.62 | -8.55 | +351 | -5.3%
Sig 2 (TS) | Full Prevention | -5.50 | -17.93 | +423 | -11.1%
Sig 2 (TS) | Large Prevention | -7.51 | -24.51 | +365 | -15.1%
Sig 3 (Severe) | Wall+Canal | -2.48 | -8.08 | +294 | -4.4%
Sig 3 (Severe) | Full Prevention | -6.16 | -20.09 | +387 | -10.9%
Sig 3 (Severe) | Large Prevention | -7.34 | -23.94 | +313 | -13.0%

## Slide 36
10
SECTION
CONCLUSION
Findings, observed effectiveness of prevention measures, and outlook.
JADE VALLEY FLOOD SIMULATION | DAVAO CITY
36 / 39

## Slide 37
10 CONCLUSION
37 / 39
JADE VALLEY FLOOD SIMULATION | DAVAO CITY, PHILIPPINES
FINAL BUILD 100%
FINDINGS
The 100% master simulation matrix demonstrates a consistent, monotonic improvement as additional prevention measures are layered:
OBSERVATION 1 Light Rain (15 mm / 2 h) produces no measurable flooding under any configuration — the subdivision can absorb light convective events without intervention.
OBSERVATION 2 Wall+Canal alone reduces peak flooded area by 5–24% across the moderate-to-heavy band. The retention basin and elevated road extend the reduction to 11–41% (full prevention) and 13–41% (large-scale prevention) — the basin contributes the largest single reduction at moderate intensities.
OBSERVATION 3 Peak depth can rise slightly with prevention: water concentrates in the basin sink while spread shrinks. The relevant decision metric is therefore extent (% / ha), not depth alone.
OBSERVATION 4 Onset time is unchanged by prevention measures — they reduce extent, not timing. Early-warning systems remain essential.

## Slide 38
10 CONCLUSION
38 / 39
CLOSING NOTES
The Jade Valley Flood Simulation system successfully models the hydrological behaviour of a real-world Philippine subdivision under the full spectrum of PAGASA-classified storm conditions.
By combining D8 terrain-based flow routing, scenario-adaptive river overflow via BFS dilation, and Green-Ampt-inspired infiltration, the model captures the essential dynamics of urban flooding at a computationally accessible scale.
The three-build hierarchy plus the 100% master orchestrator provides quantitative, frame-by-frame comparison of flood extent with and without each prevention measure. The master CSV/JSON exports support direct use in infrastructure planning, community disaster preparedness, and policy recommendations for flood-vulnerable residential areas such as Jade Valley.

## Slide 39
END OF PRESENTATION
Flood Risk Si
Davao City, Philippines | Final Project
See Documents/USER_GUIDE.md and Documents/User_Guide.docx for installation and usage instructions.
JADE VALLEY FLOOD SIMULATION | DAVAO CITY
39 / 39